## Slide 1
Crowd management based on direct communication technology
Christina Maria Mayr
Doctoral Defense
10th July, 2024
Technical University of Munich
Hochschule München University of Applied Sciences

## Slide 2
Crowd management ensures safety and comfort
Several approaches are used in practice [1]
Staff
Christina Maria Mayr | Doctoral defense | Crowd Management 2

## Slide 3
Infrastructure is often missing at transportation hubs
Inform the crowd through mobile applications?
Images: Wolfram Schlenker, rights granted
Christina Maria Mayr | Doctoral defense | Crowd Management 3

## Slide 4
Direct communication for crowd management applications?
Vehicles exchange data through direct communication technologies.
Example: IEEE 802.11p [2]
?
Christina Maria Mayr | Doctoral defense | Crowd Management 4

## Slide 5
How can crowds be redirected with mobile applications
based on direct communication technology?
Christina Maria Mayr | Doctoral defense | Crowd Management 5

## Slide 6
How can crowds be redirected with mobile applications
based on direct communication technology?
Christina Maria Mayr | Doctoral defense | Crowd Management 6
Direct communication technology:
Does the information dissemination work?
Staff
?
?

## Slide 7
How can crowds be redirected with mobile applications
based on direct communication technology?
Christina Maria Mayr | Doctoral defense | Crowd Management 7
Direct communication technology:
Does the information dissemination work?
Route recommendation algorithm:
Which one is suitable?
?

## Slide 8
Direct communication technology:
Does the information dissemination work?
Route recommendation algorithm:
Which one is suitable?
Crowd:
How to design messages to foster compliance?
How can crowds be redirected with mobile applications
based on direct communication technology?
Christina Maria Mayr | Doctoral defense | Crowd Management 8

## Slide 9
Focus of today
Christina Maria Mayr | Doctoral defense | Crowd Management 9
Novel simulator flowcontrol
Novel simulator CrowNet
Uncertainty of parameters
=
Thesis
Thesis
Thesis
Algorithm
Mobile network
Crowd
Novel socio-technical system
Component investigation
Mobile network
Algorithm
Crowd behavior
Survey
Modeling & Simulation
Modeling & Simulation
Proof of concept
Real life use case

## Slide 10
Novel model of a crowd guidance system
Map perspective System perspective
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 10
See Fig. 3.1 & 4.27 of my thesis

## Slide 11
Which route recommendation algorithm is suitable?
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 11

## Slide 12
Algorithms have been designed for fully controllable fluids –
a crowd does not behave like a fluid!
State-of-the-art algorithms:
Proportional Integral control [7], On-Off-control [8], State-space control [9-12], Model predictive control [13], …
Snapshot of a crowd simulation
150m x 25m
Christina Maria Mayr | Doctoral defense | Crowd Management 12
Congestion

## Slide 13
Recommend the route where the density is the lowest
My algorithm resolves congestion and compensates missing compliance [6]
Density in ped/m²
Short route Medium route Long route
0.0 0.5 1.0 0.5 1.0 0.5 1.0
Compliance rate
0.0
1.0
2.0
Christina Maria Mayr | Doctoral defense | Crowd Management 13
Congestion
Compensation

## Slide 14
A density-based algorithm succesfully resolves congestion
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 14
Detailed comparison of algorithms:
See my publication “Guiding …” [6]

## Slide 15
Does the information dissemination work?
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 15

## Slide 16
Testing direct communication under worst case conditions
Simple technology Extreme signal modeling Scenario
IEEE 802.11p
[2]
IEEE 802.11bd
[14]
LTE V2X
[15-19]
5G V2X
[20-26]
No signal
Niche
Christina Maria Mayr | Doctoral defense | Crowd Management 16
Cellular
WLAN

## Slide 17
17

## Slide 18
The crowd is successfully informed after several seconds
Christina Maria Mayr | Doctoral defense | Crowd Management 18
Parameter studies:
See my publication
“Analysis of info …” [27]

## Slide 19
Direct communication is suitable for redirecting crowds
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 19
Parameter studies:
See my publication
“Analysis of info …” [27]

## Slide 20
How to design mobile messages to foster compliance?
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 20

## Slide 21
Image: Wolfram Schlenker,
rights granted
Metro station (surface level)
Münchner Freiheit
Munich, Germany
21
©OpenStreetMap
openstreetmap.org/copyright
Long route
Medium route
Short route

## Slide 22
Online survey [28]: testing the effect of three message elements
Christina Maria Mayr | Doctoral defense | Crowd Management 22
Congestion information
Appeal to fans’ team spirit
Top-down view

## Slide 23
Online survey [28]: design of the survey
Assumption: fans share a social identity (the control group does not)
Christina Maria Mayr | Doctoral defense | Crowd Management 23
Fans 921 participants
Control 444 participants
The combination of the three elements leads to 8 message designs:

## Slide 24
“How likely is it that you take the short, medium and long route?”
Christina Maria Mayr | Doctoral defense | Crowd Management 24
Kruskal-Wallis test
Participants rated the attractiveness of the short ( ), medium ( ), and long ( ) route (5-point Likert scale)

## Slide 25
There are differences in between message designs
Christina Maria Mayr | Doctoral defense | Crowd Management 25
Fans: Short route Medium route Long route
Control: Short route Medium route Long route
Significant difference (p < 0.05)
Significant difference (p < 0.05)
Significant difference (p < 0.05)
Significant difference (p < 0.05)
Significant difference (p < 0.05)
Results of Kruskal-Wallis tests:

## Slide 26
Mann-Whitney U test:
p = 0.0069, W = 4157
Christina Maria Mayr | Doctoral defense | Crowd Management 26
Appealing to fans’ “team spirit” can foster compliance
Analysis of all combinations:
See my publication “Designing …” [28]
Fans:
Adding “team spirit” made the long route more attractive in one combination [27].

## Slide 27
There is no ideal message design
Crowd
Algorithm
Density sensor
Mobile app
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 27
Additional result from the survey:
Realistic route choice probabilities
See my publication “Designing …” [28]

## Slide 28
Measuring densities using direct communication
Crowd
Algorithm
Density map app
Mobile app
Route
Density
Direct
communication
Direct
communication
I use the decentralized density map application (LTE sidelink, controlled mode) [28]:
Christina Maria Mayr | Doctoral defense | Crowd Management 28

## Slide 29
Can the proposed system resolve safety-critical congestion?
I model, implement and simulate the overall system in CrowNet:
Crowd
Algorithm
Density map app
Mobile app
Route
Density
Direct
communication
Direct
communication
Christina Maria Mayr | Doctoral defense | Crowd Management 29

## Slide 30
Image: Wolfram Schlenker,
rights granted
Crowd simulation
Münchner Freiheit
Munich, Germany
Compliance: 40% [28]
30
Realistic modeling:
App usage:
40% [30]

## Slide 31
Without guidance: congestion along the short route
Density in ped/m²
31

## Slide 32
The guidance system resolves safety-critical congestion
Density in ped/m²
Area where app shows redirections
32

## Slide 33
How can crowds be redirected with mobile applications
based on direct communication technology?
Christina Maria Mayr | Doctoral defense | Crowd Management 33
Crowd
Algorithm
Density map app
Mobile app
Route
Density
Direct
communication
Direct
communication
The system resolves safety-critical congestion.
Proof of concept:

## Slide 34
I modeled and simulated a novel crowd guidance system
Christina Maria Mayr | Doctoral defense | Crowd Management 34
Algorithm
Mobile network
Crowd
Novel socio-technical system
Multi-method investigation
Direct communication
Algorithm
Crowd behavior
Survey
Modeling & Simulation
Modeling & Simulation
Next step
Build the system
Validate the system
Novel simulator CrowNet
github.com/roVer-HM/crownet
Validated
models
Thesis
Proof of concept
Real life use case
Survey data
The system resolves congestion
See my publications [6,27,28]

## Slide 35
Conclusion
A system was proposed that detects and redirects crowds through mobile applications.
It is possible to redirect crowds using mobile applications based on direct communication technology.
The proposed system can resolve safety-critical jams even when only a part of the crowd uses the technology.
Christina Maria Mayr | Doctoral defense | Crowd Management 35

## Slide 36
Claudio Feliciani, Kenichiro Shimura, and Katsuhiro Nishinari. Introduction to Crowd Management. Managing Crowds in the Digital Era: Theory and Practice. 1st ed. Springer Cham, 2021. doi: 10.1007/978-3-030-90012-0.
802.11 WG Wireless LAN Working Group. IEEE 802.11p-2010. Tech. rep. IEEE standards association, 2010.
Stefan Schuhbäck et al. Towards a Bidirectional Coupling of Pedestrian Dynamics and Mobile Communication Simulation. In: Proceedings of the OMNeT++ Community Summit 2019. 2019. doi: 10.29007/nnfj.
Benedikt Kleinmeier, Benedikt Zönnchen, Marion Gödel, Gerta Köster. Vadere: An open-source simulation framework to promote interdisciplinary understanding. In: Collective Dynamics (4). 2019. doi: 10.17815/CD.2019.21
Antonio Virdis, Michael Kirsche (eds). Recent Advances in Network Simulation. Springer Pub. 2019. doi:10.1007/978-3-030-12842-5
Christina Maria Mayr and Gerta Köster. Guiding crowds when facing limited compliance: Simulating strategies. In: PLOS ONE 17.11 (Nov. 2022), pp. 1-24. doi: 10.1371/journal.pone.0276229.
H. Ren, Y. Yan, and F. Gao. Variable guiding strategies in multi-exits evacuation: Pursuing balanced pedestrian densities. In: Applied Mathematics and Computation 397 (2021). doi: 10.1016/j.amc.2021.125965.
F. Gao et al. Effect of density control in partially observable asymmetric-exit evacuation under guidance: Strategic suggestion under time delay. In: AppliedMathematics and Computation 418 (2022). doi: 10.1016/j.amc.2021.126838.
Pushkin Kachroo et al. Pedestrian Dynamics: Feedback Control of Crowd Evacuation. Springer, 2010. doi: 10.1007/978-3-540-75561-6.
Apoorva Shende, Mahendra Singh, and Pushkin Kachroo. Optimization-Based Feedback Control for Pedestrian Evacuation From an Exit Corridor. In: IEEE Transactions on Intelligent Transportation Systems 12 (Dec. 2011), pp. 1167-1176. doi: 10.1109/TITS.2011.2146251.
Apoorva Shende, Mahendra P. Singh, and Pushkin Kachroo. Optimal Feedback Flow Rates for Pedestrian Evacuation in a Network of Corridors. In: IEEE Transactions on Intelligent Transportation Systems 14.3 (2013), pp. 1053-1066. doi: 10.1109/TITS.2013.2250965.
Zhe Zhang, Limin Jia, and Yong Qin. “Level-of-Service Based Hierarchical Feedback Control Method of Network-Wide Pedestrian Flow”. In: Mathematical Problems in Engineering 2016 (Jan. 2016), pp. 1-4. doi: 10.1155/2016/9617890.
Marcel Menner et al. MPC-based Pedestrian Routing for Congestion Balancing. Mitsubishi Electric Research Laboratories, 2023.
802.11 WG Wireless LAN Working Group. IEEE 802.11bd-2022 - IEEE Standard for Information Technology -Telecommunications and Information Exchange between Systems Local and Metropolitan Area Networks - Specific Requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY). Specifications Amendment 5: Enhancements for Next Generation V2X. Tech. rep. Mar. 10, 2023.
References (1/2)

## Slide 37
3GPP Technical Specification Group Services and System Aspects. TR 22.885 Study on LTE Support for Vehicle to Everything (V2X) Services (Release 14). Tech. rep. 2015.
3GPP Technical Specification Group Services and System Aspects. TR 36.885 Study on LTE-Based V2X Services (Release 14). Tech. rep. 2016.
3GPP Technical Specification Group Services and System Aspects. 3GPP TS 22.185 Service Requirements for V2X Services (Release 16). Tech. rep. 2020.
3GPP Technical Specification Group Services and System Aspects. TS 23.285 Architecture Enhancements for V2X Services (Release 16). Tech. rep. 2020
3GPP Technical Specification Group Radio Access Network. TS 36.213 Evolved Universal Terrestrial Radio Access (E-UTRA); Physical Layer Procedures (Release 16). Tech. rep. 2020.
3GPP Technical Specification Group Services and System Aspects. TR 22.886 Study on Enhancement of 3GPP Support for 5G V2X Services (Release 16). Tech. rep. 2018.
3GPP Technical Specification Group Radio Access Network. TR 38.885 Study on NR Vehicle-to-Everything (V2X) (Release 16). Tech. rep. 2019.
3GPP Technical Specification Group Services and System Aspects. TS 23.287 Architecture Enhancements for 5G System (5GS) to Support Vehicle-to-Everything (V2X) Services (Release 16). Tech. rep. 2020.
3GPP Technical Specification Group Services and System Aspects. TS 22.186 Enhancement of 3GPP support for V2X scenarios (Release 16). Tech. rep. 2019.
3GPP Technical Specification Group Radio Access Network. TS 38.213 Physical Layer Procedures for Control (Release 16). Tech. rep. 2020.
3GPP Technical Specification Group Radio Access Network. TS 38.321 Medium Access Control (MAC) Protocol Specification (Release 16). Tech. rep. 2020.
3GPP Technical Specification Group Radio Access Network. TS 37.895 Overall Description of Radio Access Network (RAN) Aspects for Vehicle-to-Everything (V2X) Based on LTE and NR (Release 16). Tech. rep. 2020.
Christina Maria Mayr, Stefan Schuhbäck, Lars Wischhof, Gerta Koster. Analysis of information dissemination through direct communication in a moving crowd. Safety Science (142) 105386. doi: 10.1016/j.ssci.2021.105386
Christina Maria Mayr, Anne Templeton, and Gerta Köster. Designing mobile application messages to impact route choice: A survey and simulation study. In: PLOS ONE 18.4 (Apr. 2023), pp. 1–20. doi: 10.1371/journal.pone.0284540.
Stefan Schuhbäck, Lars Wischhof, and Jörg Ott. Cellular Sidelink Enabled Decentralized Pedestrian Sensing. In: IEEE Access 11 (2023), pp. 13349-13369. doi: 10.1109/access.2023.3242946.
Fernando Fonseca et al. Use and Perceptions of Pedestrian Navigation Apps: Findings from Bologna and Porto. In: ISPRS International Journal of Geo-Information 10.7 (2021). doi: 10.3390/ijgi10070446.
References (2/2)

## Slide 38
CrowNet: a novel simulation framework
Initial simulator coupling [3]: Vadere [4] and OMNeT++ [5]
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
OMNeT++ Vadere
Christina Maria Mayr | Doctoral defense | Crowd Management 38

## Slide 39
My major contribution to CrowNet: flowcontrol
I developed flowcontrol [6] and integrated it:
Crowd
Algorithm
Density sensor
Mobile application
Route
Density
Direct
communication
Direct
communication
flowcontrol OMNeT++ Vadere
Christina Maria Mayr | Doctoral defense | Crowd Management 39

## Slide 40
Algorithm study
Alternative algorithm
Parameter settings:
Route recommendation: every 2s
Corridor width = 2.5m
Inflow = 1.6ped/(ms) “8 agents every 2s” (=30*8ped/2.5m/60s) (4ped/s)
Christina Maria Mayr | Doctoral defense | Crowd Management 40

## Slide 41: Information dissemination study

## Slide 42: Message design
Dropout: 44.51%
Number of participants who completed the survey: 444 (control), 921 (fans)

## Slide 43
Message design study
Christina Maria Mayr | Doctoral defense | Crowd Management 43

## Slide 44
Algorithm study
Alternative algorithm
Density in ped/m²
Short route Medium route Long route
0.0 0.5 1.0 0.5 1.0 0.5 1.0
Compliance rate
0.0
1.0
2.0
Christina Maria Mayr | Doctoral defense | Crowd Management 44

## Slide 45
Can appeal to fans’ “team spirit” foster compliance? (see [27])
45

## Slide 46: Density map application

## Slide 47: System test
Route recommendation: every 2s possible
Short corridor: Corridor width = 1.75m
Inflows:
Bus arrivals: 60peds/min
Counterflow: 40peds/min
Route distributions without recommendations: 49% short, 30% medium, 22% long
Route distribution when the long route is recommended: 25% short, 35% medium, 40% long

## Slide 48
Participants ranked the attractiveness of the 3 routes
Christina Maria Mayr | Doctoral defense | Crowd Management 48
5-point scale

## Slide 49: Kruskal Wallis test
The Kruskal–Wallis test by ranks “one-way ANOVA on ranks [1]”
non-parametric method
testing whether samples originate from the same distribution
extends the Mann–Whitney U test
Assumptions:
It is used for comparing two or more independent samples
equal or different sample sizes.
H_0: The mean ranks ( ~ “medians”) are equal across 3+ populations.
The smaller the p value, the more likely the null hypothesis must be rejected.
“ p < 0.05 “ -> reject H_O -> “The mean ranks are equal” is false -> difference
“ p >= 0.05 “ -> confirm H_O -> “The mean ranks are equal” is true -> no difference

## Slide 50
H_0: The mean ranks are equal across 3+ populations.

## Slide 51
There is no ideal message design
Christina Maria Mayr | Doctoral defense | Crowd Management 51
Control group
Short |  |  |  | 
Medium |  |  |  | 
Long |  |  |  | 
Short |  |  |  | 
Medium |  |  |  | 
Long |  |  |  | 
Short |  |  |  | 
Medium |  |  |  | 
Long |  |  |  | 
Fans
Short |  |  |  | 
Medium |  |  |  | 
Long |  |  |  | 
Short |  |  |  | 
Medium |  |  |  | 
Long |  |  |  | 
Short |  |  |  | 
Medium |  |  |  | 
Long |  |  |  | 
Results of the Mann-Whitney U tests: p-Value < 0.05
Congestion info Top-down view “Team spirit”
Congestion info Top-down view “Team spirit”

## Slide 53
Online survey [28]: football fans and control group, 8 designs
Assumption: fans share a social identity (the control group does not)
Christina Maria Mayr | Doctoral defense | Crowd Management 53
Fans 921 participants
Control 444 participants

## Slide 54
Does a message element have an effect?
Christina Maria Mayr | Doctoral defense | Crowd Management 54
Fans: Short route
+

## Slide 55
Christina Maria Mayr | Doctoral defense | Crowd Management 55
Fans: Short route
Does a message element has an effect?

## Slide 56: simu5G: model structure

## Slide 57
Resource Blocks (RBs)